## Slide 1: Basic Computer Architecture
Unit 3

## Slide 2
Computer Architecture
  Computer Architecture refers to those attributes of a system visible to a programmer or, put another way, those attributes that have a direct impact on the logical execution of a program.
Computer Organization
  Computer organization refers to the operational units and their interconnections that realize the architectural specifications.

## Slide 3
History of Computer Architecture

## Slide 4
Computer Architecture
The design ,arrangement, construction or organization of the different parts of a computer system is known as Computer Architecture
Computer architecture defines the way hardware components are connected together to form a computer system
Computer architecture deals with high level design issues such as Instruction sets, Addressing modes, Data types, Cache optimization etc.
It helps us to understand the functionalities of a system.
It acts as an interface between hardware and software

## Slide 5
Brief History of Computer Architecture
First Generation (1945-1958)
Vacuum Tubes
Machine code
CPU was unique to that machine
Use of drum or magnetic core memory, programs are loaded using paper tape or punch cards
2 Kb memory, 10 KIPS(thousands instruction per second)

## Slide 6
Architecture for a Computing Machine
Based on the storage and signaling of instruction and data.
Harvard architecture: uses physically separate storage and signal pathways for instructions and data. (Harvard Mark I). it stored instructions on punched tape and data in relay latches.
Von Neumann architecture: a single storage structure to hold both set of instructions and data Aka stored program computers.

## Slide 7
Second Generation(1958-1964)
Transistors – small, low-power, low-cost, more reliable than vacuum tube
Magnetic core memory
Reduced computational time to microseconds
High level languages
First OS handled one program at a time

## Slide 8
Third Generation(1964-1974)
Integrated circuits, combined thousands of transistors on a single chip using LSI
Semiconductor Memory
Timesharing, Graphics and Structured programming
2 Mb memory, 5 MIPS
Use of Cache memory

## Slide 9
Fourth Generation(1974- Present)
Microprocessor, combined millions of transistors using VLSI and ULSI technology
Single Chip processor and the single board computer emerged
Creation of the Personal computer(PC)
Object oriented programming and Artificial intelligence concept
Intel 4004 was the worlds first universal microprocessor.

## Slide 10
Self Study !!
ENIAC
Whirlwind computer
UNIVAC
IBM 7090
IBM System/360
Intel 4004

## Slide 11: Microoperations
The operation executed on data stored in registers are called micro operations.
A micro operation is elementary operation performed on the information stored in one or more registers.
The result of operation may replace the previous binary information of register or may be transferred to other register.
Example: shift, count, clear and load.

## Slide 12: Instruction Codes
Basic computer is smaller in comparison to commercial computer.
Organization of the computer is defined by its internal register, the timing and control structure and set of instructions and its uses.
The general purpose digital computer is capable of executing various sequence of micro operations. It performs on data stored in registers
The user of computer can control the process by means of a program which is set of instructions that specify the operations and operand.

## Slide 13: Instruction Codes
Computer instruction
  Is a binary code that specifies a sequence of micro operations for computer
  Instruction code and data are stored in memory
  Computer read each instruction from memory and keep in register
  Control interprets the binary code of instructions and proceed to execute it by issuing a sequence of micro operations.
  Every computer has its own unique instruction set.

## Slide 14: Instruction Codes
  Instruction code is group of bits that instruct computer to perform a specific operations.
It is usually divided into 2 parts:
  Operation code
    If n bits are in operation code, then there are distinct operations.
    Operation can be add, subtract, multiply, shift, complement etc.
    The control unit receives the instruction from memory and interprets the operation code bits and then issues a control signals to initiate microperations on internal computer registers.
  Operand code

## Slide 15: Stored Program Organization

## Slide 16: Addressing Modes of basic computer (Direct and Indirect addressing mode)
When the second part of an instruction code specifies the address of an operand, the instruction is said to have a Direct address.
When the second part of an instruction code specifies the address of a memory word in which the address of the operand is available, the instruction is said to have Indirect address.

## Slide 17: Addressing Modes of Basic computer (Direct and Indirect addressing mode)

## Slide 18: Addressing Modes of Basic computer (Direct and Indirect addressing mode)
The indirect address instruction needs two references to memory to fetch an operand.
  The first reference is needed to read the address of the operand.
  Second reference is for the operand itself.

## Slide 19: Addressing Modes of basic computer (Direct and Indirect addressing mode)

## Slide 20: Computer Registers
Basic computer have memory and Processors.
Memory have capacity=4096 words=
1 word=16 bits

## Slide 21: Computers Registers
DR (Data registers)-To hold operand read from memory. 16 bits
AC (Accumulator)- General purpose register, used for storing intermediate arithmetic and logic results. 16 bits
IR(Instruction Register)- Instruction fetched from memory are placed in IR. 16 bits
TR(Temporary Registers)- used for holding temporary data. 16 bits

## Slide 22
AR(Address registers)- holds address for memory. 12 bits
PC(Program counter)- Address of next instruction. 12 bits
INPR(Input Register)-receives 8 bit input from input device. 8 bits
OUTR(Output Registers)-hold 8 bit character for output. 8 bits

## Slide 23: Why common bus system is used?
Basic computer has eight registers, a memory unit and a control unit.
Path must be provided to transfer information from one register to another and between memory and register.
The number of wires will be excessive if connections are between the outputs of each register and input of other registers.
So efficient way is to use common bus system.

## Slide 24: Common Bus system

## Slide 25: Computer Instructions
Memory reference instructions-instruction that has operand addresses referring to a location in memory
Register Reference Instructions-specifies a operation on AC or a test of the AC
Input Output instructions-used to input data / output data

## Slide 26: Computer Instruction Format with its types

## Slide 27: Basic Computer Instructions

## Slide 28: Instruction Set Completeness
Instruction set is complete if it contains sufficient set of instructions in each of following categories-
  Arithmetic, logical and shift instruction
  Instruction for moving information to and from memory and processor registers.
  Program control instructions together that check status conditions(E.g Branch)
  Input and Output Instructions

## Slide 29: Control Unit
Control Unit is implemented In 2 ways:-
Hardwired Control – CU is made up of sequential and combinational circuits to generate the control signals. – If logic is changed we need to change the whole circuitry – Expensive – Fast
Micro programmed Control – A control memory on the processor contains micro-programs that activate the necessary control signals. – If logic is changed we only need to change the micro-program. – Cheap – Slow

## Slide 30: Control Unit of Basic Computer

## Slide 31: Instructions cycle
Program is executed in computer by going through a cycle for each instruction. Each instruction cycle is subdivided into different phases-
  1. Fetch an instruction from memory. 2. Decode the instruction. 3. Read the effective address from memory if the instruction has an indirect address. 4. Execute the instruction.

## Slide 32: Fetch and decode
Initially PC is loaded with address of first instruction .
Sequence counter SC is cleared to 0, providing After each clock pulse SC is Incremented and timing sequence go through , , and so on.

## Slide 33: Fetch and Decode
The micro operations for the fetch and decode phases can be specified by the following register transfer statements:

## Slide 34: Fetch Phase

## Slide 35: Determine the type of instruction
After decoding the timing signal is
Control unit determine the type of instruction just read from memory.
There are 3 type of instruction.
  =1, opcode=111
    Instruction can be register reference or input/output type.
    I=0 register reference
    i=1 I/O reference
  =0, opcode=000 to 110
    Instruction is memory referenced.
    I=0 direct addressing
    I=1 indirect Addressing

## Slide 36: Flowchart of instruction cycle

## Slide 37: Register –Reference Instructions
Register Reference Instructions are identified when - D7 = 1, I = 0 - Register Ref. Instr. is specified in b0 ~ b11 of IR - Execution starts with timing signal T3

## Slide 38: Register –Reference Instructions

## Slide 39: Memory Reference Instructions