## Slide 1: Microprogrammed Control
Unit 4

## Slide 2: Design of Accumulator logic

## Slide 3: Change AC

## Slide 4: Gate Structure For Controlling AC

## Slide 5: Control unit
Initiate sequence of microoperations
Number of microoperations are finite

## Slide 6: Control Unit
Control Unit is implemented In 2 ways:-
Hardwired Control – fixed instructions, fixed logic block, encoder, decoder.
  -CU is made up of sequential and combinational circuits to generate the control signals. – If logic is changed we need to change the whole circuitry – Expensive – high speed operations.
  -complex
  -no flexibility of adding instructions
  -Intel 8085,motorola 6802,RISC.

## Slide 7
Micro programmed Control – A control memory on the processor contains micro-programs that activate the necessary control signals. – If logic is changed we only need to change the micro-program. – Cheap – Slow
-Intel 8080,Motorola 68000, CISC.

## Slide 8
Hardwired Control

## Slide 9: Introduction
Control logic is implemented with gates, flip flops, decoder and other digital circuits.
If logic is changed we need to change the whole circuitry
Expensive
Fast

## Slide 10: Timing And Control
Generated by 4-bit sequence counter and 4x16 decoder.  The SC can be incremented or cleared.  Example: T0, T1, T2, T3, T4, T0, T1 . . .

## Slide 11: Timing Signal

## Slide 12: Control Unit Of Basic Computer

## Slide 13
Control Memory

## Slide 14: Control Word
Control function specifies a microoperation is a binary variable.
When it is in one binary state microoperation is executed.(other doesn’t change)
Active state can be 1 or 0 depending on application.
Control variables at any given time can be represented by string of 0’s and 1’s called control word.

## Slide 15: Control Memory
  Contains 2 memory
    Main Memory
      Used to store program
      Content can be altered
    Control Memory
      Located in control unit
      Contains fixed microprogrammed that can’t be altered by occasional user.
      Consists of microinstructions
      Microinstructions specify various register microoperations.

## Slide 16: Microinstruction
Each word in control memory is microinstruction.
Microinstruction specifies one or more microoperations.
Sequence of microinstructions are Microprogram.
Advance technology-Dynamic programming
  Microprogram loaded from auxiliary device.
  Writable control memory.
  But control memory are mostly used for reading.

## Slide 17
Micro programmed Control

## Slide 18
Control word
  It is a string of control variables (0’s and 1’s) occupying a word in control memory.
Microprogram
  Program stored in control memory that generates all the control signals required to execute the instruction set correctly
  Consists of microinstructions

## Slide 19
Microinstruction  Contains a control word and a sequencing word  Control Word – contains one or more microoperations  Sequencing Word - Contains information needed to decide the next microinstruction address .

## Slide 20: Micro Programmed Control Organization

## Slide 21: Microprogrammed control Organization
Control memory is ROM, within which all control information is permanently stored.
Control memory Address Register specifies the address of microinstruction.
Control Data Register holds the microinstruction read from memory.

## Slide 22: Microprogrammed control Organization
Microinstructions contains control word that specifies one or more microoperations.
After execution the location of next microinstruction must be determine.
  Address can be in sequence or out of sequence.
  So, some bits of present microinstruction are used to determine the next address of microinstruction.
Next address is calculated in next address generator.
  Also know as sequencer.(Determine next address in sequence)

## Slide 23: Address Sequencing (Introduction)
Microinstructions are stored in control memory in groups.
  Called routine.
  Every computer instruction has its own microprogram routine in control memory, which generate sets of microoperations to execute that instruction.
  Hardware that control address sequencing of control memory must be capable of sequencing microinstructions within routine or may able to branch from one routine to other.

## Slide 24: Steps for execution of single computer instruction
Control address register is loaded with initial address when computer is on- may be fetch routine.
Fetch routine is sequenced by incrementing CAR.
At END of routine instruction is in IR.

## Slide 25
Calculating Effective Address of operand.
Can be reached through branch microinstruction.
At END operand address is available in memory Address Register.

## Slide 26
Execute Instruction
Opcode determine which routine should be run for execution of particular operation.
Each instruction has its own microprogram routine.
Mapping process
  Process of transformation from opcode bit to an address in control memory where routine is located.

## Slide 27: Address sequencing capabilities required in control memory
Incrementing of Control Address register.
Unconditional branch or conditional branch depending on status bit.
A mapping process from bit of instruction to control memory address.
A facility of subroutine call and return.

## Slide 28: Block Diagram of Address Sequencer

## Slide 29: Conditional Branching
If Condition is true, set the appropriate field of status register to 1. Conditions are tested for
  O (overflow),
  N (negative),
  Z (zero) and C(carry)
  Then test the value of that field if the value is 1 take branch address from the next address field of the current microinstruction Otherwise simple increment the address.

## Slide 30: Unconditional branching
Fix the value of one status bit at the input of the multiplexer to 1. So that always branching is done.

## Slide 31: Subroutine
Subroutine are program that are used by other routine to accomplished a particular task.
Subroutine can be called at any point in main program.
Some subroutine are frequently used in many routine.
E.g calculation of EA is common to all memory reference instruction.

## Slide 32
When subroutine is called the incremented address is save in Subroutine register.
Register are arranged as stack- used in LIFO manner

## Slide 33: Microprogram
After Microprogrammed Control unit is established
  Designer generate microcode for control memory(Microprogramming)

## Slide 34: Computer Configuration

## Slide 35: Microinstructions

## Slide 38: Symbolic Microinstruction
Symbols like ADD,CLRAC,READ,COM etc are used to specify microinstructions.
Assembler is used to translate symbolic microinstruction to its binary equivalent.
Contains five fields:-
  Label:-This field may be empty or it may specify a symbolic address. A label is terminated with colon(:).
  Microoperations field:- contains one, two or three symbols separated by commas.
  CD:- one of U, I,S,Z.
  BR- can contains 4 symbols. JMP,CALL,RET,MAP.

## Slide 39
  AD-With symbolic address
      With Symbol NEXT to designate the next address in sequence.
      When BR field contains RET or MAP Symbol, the AD field is left empty and is converted to 7 zeroes by assemblers.
  ORG- origin address

## Slide 40: FETCH ROUTINE Example

## Slide 41: Binary Microprogram
Program not Stored in memory in Symbolic form.
Translated by assembler.

## Slide 42: Design of Control Unit

## Slide 43: Microprogram Sequencer
Basic component of microprogrammed are
  Control memory and next address generator
Address selection part is microprogram sequencer.
It load CAR with address of microinstruction to fetch and execute next microprogram.
Control unit doesn’t contain one register but stack of SBR.

## Slide 44: Microprogram Sequencer